## Slide 1
Medical Robotics Group Coursework
Group 14:
Gavin Z Yue (02469416)
Xinru Yan (02450945)
Zakariya Ali (02354549)

## Slide 2
Task 1
Robot Modelling and MDH Table

## Slide 3
frame i | a（i-1） | alpha（i-1） | d（i） | theta（i）
1 | 0 | 0 | 127 | 0+θ1
2 | 29.69 | 90 | 0 | 90+θ2
3 | 108 | 0 | 0 | 0+θ3
4 | 20 | 90 | 168.98 | 0+θ4
5 | 0 | -90 | 0 | -90+θ5
6 | 0 | 90 | 24.29 | 0+θ6
MDH for CoppeliaSim
Task 1
Task 1 :MDH Table 1
base
J6
J3
J2
J1
J4 J5
Origin of frames
Defined frames

## Slide 4
frame i | a（i-1） | alpha（i-1） | d（i） | theta（i）
1 | 0 | 0 | 127 | 0+θ1
2 | 29.69 | -90 | 0 | -90+θ2
3 | 108 | 0 | 0 | 0+θ3
4 | 20 | -90 | 168.98 | 0+θ4
5 | 0 | +90 | 0 | +90+θ5
6 | 0 | -90 | 24.29 | 0+θ6
Z4
X1
Y1
Z1
X2
Y2
Z2
X3
Y3
Z3
X4
Y4
Z4
X5
Y5
Z5
X6
Y6
Z6
X0
Y0
Z0
MDH for Real Robot
Task 1
Task 1 :MDH Table 2

## Slide 5
Task 2
Joint Space Control

## Slide 6
Task 2: Model
Initial Pose
Intermediate Pose
Final Pose
Path 2
 | Angular limit (deg) |  | Velocity limit (deg/s)
J1 | -110 | 160 | 85
J2 | -35 | 70 | 60
J3 | -120 | 60 | 65
J4 | -180 | 180 | 200
J5 | -200 | 30 | 200
J6 | -360 | 360 | 450
Quintic Polynomial
Path Planning
Result
Forward Kinematics
End-Effector Position
In Cartesian Space
Guarantee Joint Limits
Path 1
Notes: finished

## Slide 7
Task 2: Validation
Trajectory Validation
In Matlab
In Coppelia

## Slide 8
Task 3
Cartesian Space Control

## Slide 9
Task 3
Path Planning
InitialPose
IntermediatePose
FinalPose
Straight line
Path Planning in
Cartesian Space
Inverse Kinematics
Jacobian, Joint limits
Newton Iteration
Joints Pose
Joint Movement
Trajectory
Interpolate with different gap
Interpolate with same gap
Newton Iteration don’t converge?
(1) Check for Joint limit;
(2) Set learning rate=0.5, avoid oscillation
Interpolation

## Slide 10
Task 3 : Validation
Trajectory Validation
In Matlab
In CoppeliaSim
Notes: 视频和仿真的视频

## Slide 11: Difference between Cartesian and Joint space control
Task3 : Comparison of two methods
Cartesian space control
Trajectory defined in end effector position
Easy to visualise trajectory
Joint motion derived from end effector path through inverse kinematics
Joint speeds and acceleration can be non-uniform
Instability near singularities or areas where large changes in joint spaces are required
Robot independent
Preferred when control of end effector position is key
e.g. robotic surgery, drawing etc
Joint space control
Trajectory defined in terms of joint angles/positions
Not easy to visualize trajectory
Joint motion controlled hence uniform motion
The performance is less prone to vibration
No problem with singularities
Robot dependent
Preferred method when space is limited or when carrying out tasks where control over joints is key e.g. obstacle avoidance

## Slide 12
Task 4: Robot Pick-and-Place
Three-Finger Soft Gripper
[1]

## Slide 13
Joint-Space Method
Trajectory planning using waypoints
Waypoints Initiating
Joint-Space
Jacobian & IK
Polynomial Interpolation
Path planning in Joint-Space
Joint Pose
Two main challenges:
Mount E-E
Keep Gripper Straight downwards
Task 4

## Slide 14
New DH table to extend link 6 length
frame (i) | a （i-1） | alpha（i-1） | d （i） | theta（i）
1 | 0 | 0 | 127 | 0+θ1
2 | 29.69 | -90 | 0 | -90+θ2
3 | 108 | 0 | 0 | 0+θ3
4 | 20 | -90 | 168.98 | 0+θ4
5 | 0 | +90 | 0 | +90+θ5
6 | 0 | -90 | 24.29+40 | 0+θ6
Challenge 1: Mounting E-E
New robot model with end-effector
Task 4

## Slide 15
Challenge 2: Gripper downwards
J2
J3
J5
During Jacobian and IK
Reach the destination:
No θ constraints at Point 5
Task 4

## Slide 16
Simulation Result
Angular Velocity

## Slide 18
Bonus Task
Minimally Invasive Surgery
A Robot arm with RCM point illustration [2]

## Slide 19
J3
J2
J5
RCM
J2
J3
J5
RCM
+
Passive Joint
Double parallelogram[3]
RCM
RCM
Geometry Solution

## Slide 20
Keep End-Effector Horizontal Direction
Vertical Direction
[2]
Combined with Algebra Solution
Only 3 Variables

## Slide 21
Reference
[1] WLKATA Robotics, “WLKATA Robotics Documents” Available at https://document.wlkata.com/?doc=/
[2] Locke, R.C., & Patel, R.V. (2007). Optimal Remote Center-of-Motion Location for Robotics-Assisted Minimally-Invasive Surgery. Proceedings 2007 IEEE International Conference on Robotics and Automation, 1900-1905.
[3] Kim, Sung-Kyun & Shin, Won-Ho & Ko, Seong Young & Kim, Jonathan & Kwon, Dong-Soo. (2008). Design of a compact 5-DOF surgical robot of a spherical mechanism: CURES. IEEE/ASME International Conference on Advanced Intelligent Mechatronics, AIM. 990 - 995. 10.1109/AIM.2008.4601796.

## Slide 22
Q & A
Thanks for listening!